HOLDOVER TIME TABLES

ICE PELLET ALLOWANCE TIME

HEAVY SNOW PROCEDURES

WINTER 2006-2007

Winter 2006-07 Deicing/Anti-icing Guidance

Background

In October 2005, the FAA issued Notices 8000.309, Dispatching During Precipitation Conditions of Ice Pellets, Snow Pellets, or Other Icing Events for which No Hold Over Times Exist; and 8000.313, Parts 121 and 135 Operations Specifications for Deicing/Anti-icing Operations in Ice Pellets Without Deice/Anti-ice Fluids.  As a result of these notices, industry requested the FAA conduct research to obtain data to support relief for some of the current conditions for which no holdover times exist.  That research was conducted during the winter season of 2005-06.  The following relief is a result of that research and further review of existing data.  Although these stated precipitation condition allowances are provided, the general requirement that takeoff not be attempted with any contaminant adhering to the critical surfaces of the aircraft still applies.

Operations in Light Ice Pellets (without any other forms of precipitation present)

A.  Tests have shown that ice pellets generally remain in the frozen state imbedded in Type IV anti-icing fluid, and are not absorbed by the fluid in the same manner as other forms of precipitation.  Using current guidelines for determining anti-icing fluid failure, the presence of a contaminant not absorbed by the fluid (remaining imbedded) would be an indication that the fluid has failed.  These imbedded ice pellets are generally not detectable by the human eye during pre-takeoff contamination check procedures.  Therefore, a pre-takeoff contamination check in light ice pellet conditions would not be of value and is not required.

B.  These tests have also shown that after proper deicing and anti-icing, the accumulation of light ice pellets in Type IV fluid will still sheer from the aerodynamic surfaces during takeoff.  This sheering occurs with rotation speeds consistent with Type IV recommended applications for up to 25 minutes from the start of the Type IV anti-icing fluid application.

C.  Operators with a deicing program approved in accordance with Title 14 of the Code of Federal Regulations (14 CFR) part 121, section 121.629, will be allowed, in light ice pellet conditions with no other form of precipitation present, up to 25 minutes after the start of the anti-icing fluid application to commence the takeoff with the following restrictions:

1.  The aircraft critical surfaces must be free of contaminants, or the aircraft be properly deiced prior to the application of the anti-icing fluid.

2.  This allowance time, of up to 25 minutes, is valid only if the aircraft is anti-iced with undiluted Type IV fluid.

3.  Due to the sheer qualities of Type IV fluids with imbedded ice pellets, this allowance is limited to aircraft with a rotation speed of 100 knots or greater.

4.  If the takeoff is not accomplished within the 25 minutes allowed, the aircraft must be completely deiced, and if precipitation is still present, anti-iced again prior to a subsequent takeoff.

5.  A pre-takeoff contamination check is not required.  The allowance time of up to 25 minutes cannot be extended by an internal or external check of the aircraft critical surfaces.

6.  If ice pellet precipitation becomes heavier than light or is mixed with any other form of precipitation, the 25-minute allowance time cannot be used.

Operations in Heavy Snow

A.  No holdover times exist for heavy snow conditions in the current holdover time tables.  Review of existing data from past testing has indicated with proper tactile and/or visual checks, as appropriate for the aircraft, and a determination that the fluid has not failed, takeoffs may be safely conducted.  A tactile and/or visual check in heavy snow conditions must be accomplished in a manner that provides an assessment that can be accurately accomplished.  It is imperative that the tactile and/or visual check procedures to determine if the anti-icing fluid has failed in heavy snow conditions be at least as comprehensive as the authorized procedures for the operators pre-takeoff contamination check (when holdover times have been exceeded) for those precipitation conditions for which holdover times exist.  Anti-icing fluids dissolve the snow and absorb the resulting moisture into the fluid.  When the fluid approaches its moisture saturation point, it starts to change in appearance and the snow starts to accumulate on and in the fluid.  At this stage, the fluid has failed and takeoff is not authorized.  If the operator’s procedure to accomplish this check is different from the operator’s approved pre-takeoff contamination check procedures for other precipitation conditions, this check procedure must be verified and approved by the operator’s principal operations inspector (POI).

B.  Operators with a deicing program approved in accordance with 14 CFR part 121, section 121.629, will be allowed to take off in heavy snow conditions subject to the following restrictions:

1.  The aircraft must be anti-iced with undiluted Type IV fluid.

2.  The aircraft critical surfaces must be free of contaminants, or the aircraft be properly deiced prior to the application of the anti-icing fluid.

3.  The operator must accomplish an approved tactile and/or visual check, as appropriate, of the aircraft critical surfaces within 5 minutes of takeoff.

4.  If this check is accomplished visually from within the aircraft, the view must be such that it is not obscured by de/anti-icing fluid, dirt, or fogging.  If the critical surfaces cannot be seen due to snowfall, distance from the viewing position, or inadequate lighting, or for any other reason, the check must be a visual or tactile check conducted from outside the aircraft.

5.  If a definitive fluid failure determination cannot be made using the checks prescribed, takeoff is not authorized.  The aircraft must be completely deiced, and if precipitation is still present, anti-iced again prior to a subsequent takeoff.

###### TABLE OF CONTENTS FOR HOT GUIDELINES

FOR WINTER 2006-2007

TABLE	PAGE

Table 1.  FAA Guideline for Holdover Times SAE Type I Fluid Mixtures as a Function of Weather Conditions and OAT.	1

Table 1A. FAA Guidelines for the Application of SAE Type I Fluid Mixtures.	2

Table 1B. Snowfall Intensities as a Function of Prevailing Visibility. 	3

# Table 2.  FAA Guideline for Holdover Times SAE Type II Fluid Mixtures as a Function of Weather Conditions and OAT.	4

Table 2A. FAA Guideline for Holdover Times KILFROST ABC-II PLUS Type II Fluid Mixtures as a Function of Weather Conditions and OAT.	5

Table 2B. FAA Guideline for Holdover Times KILFROST ABC-2000 Type II Fluid Mixtures as a Function of Weather Conditions and OAT.	6

Table 2C. FAA Guideline for Holdover Times KILFROST ABC-TF2 Type II Fluid Mixtures as a Function of Weather Conditions and OAT.	7

Table 2D FAA Guideline for Holdover Times OCTAGON E-MAX Type II Fluid Mixtures as a Function of Weather Conditions and OAT.	8

Table 2E FAA Guideline for Holdover Times SPCA ECOWING 26 Type II Fluid Mixtures as a Function of Weather Conditions and OAT.	9

Table 2F. FAA Guideline for Holdover Times CLARIANT SAFEWING MP II 2025 ECO Type II Fluid Mixtures as a Function of Weather Conditions and OAT.	10

Table 2G FAA Guideline for Holdover Times CLARIANT SAFEWING MP II FLIGHT Type II Fluid Mixtures as a Function of Weather Conditions and OAT.	11

Table 3.  FAA Guideline for Holdover Times SAE Type III Fluid Mixture as a Function of Weather Conditions and OAT.	12

TABLE	PAGE

Table 4.  FAA Guideline for Holdover Times SAE Type IV Fluid Mixtures as a Function of Weather Conditions and OAT.	13

Table 4A. FAA Guideline for Holdover Times DOW UCAR ULTRA+ Type IV Fluid Mixtures as a Function of Weather Conditions and OAT.	14

Table 4B. FAA Guideline for Holdover Times DOW UCAR ENDURANCE EG106 Type IV Fluid Mixtures as a Function of Weather Conditions and OAT.	15

Table 4C. FAA Guideline for Holdover Times DOW UCAR FLIGHTGUARD AD-480 Type IV Fluid Mixtures as a Function of Weather Conditions and OAT.	16

Table 4D.	FAA Guideline for Holdover Times OCTAGON MAX-FLIGHT Type IV Fluid Mixtures as a Function of Weather Conditions and OAT.	17

Table 4E. FAA Guideline for Holdover Times OCTAGON MAX-FLIGHT 04 Type IV Fluid Mixtures as a Function of Weather Conditions and OAT.	18

Table 4F. FAA Guideline for Holdover Times OCTAGON MaxFlo Type IV Fluid Mixtures as a Function of Weather Conditions and OAT	19

Table 4G. FAA Guideline for Holdover Times KILFROST ABC-S Type IV Fluid Mixtures as a Function of Weather Conditions and OAT.	20

Table 4H. FAA Guideline for Holdover Times KILFROST ABC-S PLUS Type IV Fluid Mixtures as a Function of Weather Conditions and OAT.	21

Table 4I. FAA Guideline for Holdover Times CLARIANT SAFEWING MP IV 2001 Type IV Fluid Mixtures as a Function of Weather Conditions and OAT.	22

Table 4J. FAA Guideline for Holdover Times CLARIANT SAFEWING MP IV 2012 PROTECT Type IV Fluid Mixtures as a Function of Weather Conditions and OAT.	23

Table 4K. FAA Guideline for Holdover Times CLARIANT SAFEWING MP IV 2030 ECO Type IV Fluid Mixtures as a Function of Weather Conditions and OAT	24

Table 4L. FAA Guideline for Holdover Times CLARIANT SAFEWING MP IV LAUNCH Type IV Fluid Mixtures as a Function of Weather Conditions and OAT	25

Table 4M. FAA Guideline for Holdover Times SPCA AD-480 Type IV Fluid Mixtures as a Function of Weather Conditions and OAT.	26

Table 5.  FAA Guidelines for the Application of SAE Type II, Type III, and Type IV Fluid Mixtures..	27

Table 6.  Lowest On-wing Viscosity Values for Neat SAE Type II and Type IV Fluids                                       28

Table 7.  List of Qualified Deicing/Anti-Icing Fluids – Winter 2006-2007.	29-31

### FAA TYPE I Holdover Time Guideline

### Table 1.  FAA Guideline for Holdover Times SAE Type I Fluid Mixtures as a Function of Weather Conditions and OAT.

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Approximate Holdover Times Under Various Weather Conditions (hours: minutes) |
| --- | --- |
| Degrees Celsius | Degrees Fahrenheit | Active Frost | Freezing Fog | Snow/Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
|  |  |  |  | Very Light(( | Light (( | Moderate(( |  |  |  |  |
| -3 and above | 27 and above | 0:45 | 0:11 - 0:17 | 0:18-0:22 | 0:11 - 0:18 | 0:06 - 0:11 | 0:09 - 0:13 | 0:02 - 0:05 | 0:02-0:05 |  |
| below -3 to -6 | below 27 to 21 | 0:45 | 0:08 - 0:13 | 0:14-0:17 | 0:08 - 0:14 | 0:05 - 0:08 | 0:05 - 0:09 | 0:02 - 0:05 | CAUTION: No holdover time guidelines exist |
| below -6 to -10 | below 21 to 14 | 0:45 | 0:06 - 0:10 | 0:11-0:13 | 0:06 - 0:11 | 0:04 - 0:06 | 0:04 - 0:07 | 0:02 - 0:05 |  |
| below -10 | below 14 | 0:45 | 0:05 - 0:09 | 0:07-0:08 | 0:04 - 0:07 | 0:02 - 0:04 |  |  |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

* Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 degrees Celsius (32 degrees Fahrenheit) only

‡ Heavy snow, snow pellets, ice pellets, moderate and heavy freezing rain, hail

(( TO USE THESE TIMES, THE FLUID MUST BE HEATED TO A MINIMUM TEMPERATURE OF 60(C (140(F) AT THE   NOZZLE AND AT LEAST 1

LITER/M2 (( 2 GALS/100FT2) MUST BE APPLIED TO DEICED SURFACES

SAE Type I fluid/water mixture is selected so that the freezing point of the mixture is at least 10 (C (18 (F) below OAT.

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME 
BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- SAE TYPE I FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT.															August 2006

TABLE  1A - FAA Guidelines for the Application of SAE Type I Fluid Mixtures.

Minimum Concentrations as a Function of Outside Air Temperature (OAT).

Concentrations in % volume

| Outside AirTemperature (OAT) | One-step Procedure Deicing/Anti-icing | Two-step Procedure |
| --- | --- | --- |
|  |  | First step: Deicing | Second step: Anti-icing 1, 2 |
| -3(C (27(F) and above | Mix of fluid and water heated to 60(C (140(F) minimum at the nozzle, with a freezing point of at least 10(C (18(F) below OAT | Heated water or a mix of fluid and water heated to 60(C (140 (F) minimum at the nozzle | Mix of fluid and water heated to 60(C (140(F) minimum at the nozzle, with a freezing point of at least 10(C (18(F) below OAT |
| Below -3(C (27 (F) |  | Freezing point of heated fluid mixture shall not be more than 3 (C (5 (F) above OAT |  |
| Notes: Upper temperature limit shall not exceed fluid and aircraft manufacturers’ recommendations. To use Type I holdover time guidelines in snow conditions, at least 1 liter per square meter (2 gal. Per 100 square feet) fluid must be applied to the deiced surfaces. This table is applicable for the use of Type I Holdover Time Guidelines. If holdover times are not required, a temperature of 60(C (140(F) at the nozzle is desirable. Caution: Wing skin temperatures may differ and, in some cases, be lower than OAT. A stronger mix (more glycol) can be used under these conditions. |
| To be applied before first-step fluid freezes, typically within 3 minutes. Fluids must only be used at temperatures above their lowest operational use temperature (LOUT). |

August 2006

Table 1B.  Snowfall INTENSITIES as a Function of prevailing Visibility

| Time of Day | Temp. | Visibility (Statute Mile) |  |
| --- | --- | --- | --- |
|  | Degrees Celsius | Degrees Fahrenheit | (2 1/2 | 2 | 1 1/2 | 1 | 3/4 | 1/2 | (1/4 |  |
| Day | colder/equal -1 | colder/equal 30 | Very Light | Very Light | Light | Light | Moderate | Moderate | Heavy | Snowfall Intensity |
|  | warmer than -1 | warmer than 30 | Very Light | Light | Light | Moderate | Moderate | Heavy | Heavy |  |
| Night | colder/equal -1 | colder/equal 30 | Very Light | Light | Moderate | Moderate | Heavy | Heavy | Heavy |  |
|  | warmer than -1 | warmer than 30 | Very Light | Light | Moderate | Heavy | Heavy | Heavy | Heavy |  |
| NOTE: Based upon technical report, “The Estimation of Snowfall Rate Using Visibility,” Rasmussen, et al., Journal of Applied Meteorology, October 1999 and additional in situ data. NOTE: This table is for estimating snow intensities for use with Type I, II, III, and Type IV Fluids Holdover Time Guidelines. |
| HEAVY = Caution - no holdover time guidelines exist |

August 2006

# FAA TYPE II Holdover Time Guideline

# TABLE 2 - FAA Guideline for Holdover Times SAE Type II Fluid Mixtures as a Function of Weather Conditions and Outside Air Temperature

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Type II Fluid Concentration Fluid/Water (Volume %/Volume %) | Approximate Holdover Times Under Various Weather Conditions (hours: minutes) |
| --- | --- | --- |
| Degrees Celsius | Degrees Fahrenheit |  | Active Frost | Freezing Fog | Snow/ Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
| -3 and above | 27 and above | 100/0 | 8:00 | 0:35-1:30 | 0:20-0:45 | 0:30-0:55 | 0:15-0:30 | 0:05-0:40 |  |
|  |  | 75/25 | 5:00 | 0:25-1:00 | 0:15-0:30 | 0:20-0:45 | 0:10-0:25 | 0:05-0:25 |  |
|  |  | 50/50 | 3:00 | 0:15-0:30 | 0:05-0:15 | 0:05-0:15 | 0:05-0:10 |  |  |
| below -3 to -14 | below 27 to 7 | 100/0 | 8:00 | 0:20-1:05 | 0:15-0:35 | ***0:15-0:45 | ***0:10-0:25 | CAUTION: No holdover time guidelines exist |
|  |  | 75/25 | 5:00 | 0:20-0:55 | 0:15-0:25 | ***0:15-0:30 | ***0:10-0:20 |  |
| below -14 to -25 | below 7 to -13 | 100/0 | 8:00 | 0:15-0:20 | 0:15-0:30 |  |
| below -25 | below -13 | 100/0 | SAE Type II fluid may be used below -25 °C (-13 °F) provided the freezing point of the fluid is at least 7 (C (13 °F) below the OAT and the aerodynamic acceptance criteria are met. Consider use of SAE Type I when SAE Type II fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

* Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 °C (32 °F) only

*** No holdover time guidelines exist for this condition below  -10 (C (14 (F)

‡ Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- SAE TYPE II FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT.

August 2006

## TABLE 2A - FAA Guideline for Holdover Times KILFROST ABC-II PLUS Type II Fluid Mixtures as a Function of Weather Conditions and Outside Air Temperature

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Manufacturer Specific Type II Fluid Concentration Neat-Fluid/Water (Volume %/Volume %) | Approximate Holdover Times Under Various Weather Conditions (hours: minutes) |
| --- | --- | --- |
| Degrees Celsius | Degrees Fahrenheit |  | Active Frost | Freezing Fog | Snow/ Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other ‡ |
| -3 and above | 27 and above | 100/0 | 8:00 | 1:10-2:25 | 0:25-0:55 | 0:35-1:10 | 0:30-0:40 | 0:05-1:00 |  |
|  |  | 75/25 | 5:00 | 1:10-2:25 | 0:25-0:50 | 0:30-1:00 | 0:20-0:40 | 0:05-0:50 |  |
|  |  | 50/50 | 3:00 | 0:15-0:45 | 0:15-0:35 | 0:05-0:25 | 0:05-0:15 | CAUTION: No holdover time guidelines exist |
| below -3 to -14 | below 27 to 7 | 100/0 | 8:00 | 0:30-1:05 | 0:15-0:35 | ***0:15-0:45 | ***0:10-0:30 |  |
|  |  | 75/25 | 5:00 | 0:20-0:55 | 0:15-0:35 | ***0:15-0:30 | ***0:10-0:20 |  |
| below -14 to -25 | below 7 to -13 | 100/0 | 8:00 | 0:15-0:20 | 0:15-0:30 |  |
| below -25 | below -13 | 100/0 | KILFROST ABC-II PLUS Type II fluid may be used below -25 °C (-13 °F) provided the freezing point of the fluid is at least 7 °C (13 °F) below the OAT and the aerodynamic acceptance criteria are met. Consider use of SAE Type I when KILFROST ABC-II PLUS Type II fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

* Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 degrees Celsius (32 degrees Fahrenheit) only

*** No holdover time guidelines exist for this condition below  -10 (C (14 (F)

‡ Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- KILFROST ABC-II PLUS TYPE II FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT.

August 2006

## TABLE 2B - FAA Guideline for Holdover Times KILFROST ABC-2000 Type II Fluid Mixtures as a Function of Weather Conditions and Outside Air Temperature

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Manufacturer Specific Type II Fluid Concentration Neat-Fluid/Water (Volume %/Volume %) | Approximate Holdover Times Under Various Weather Conditions (hours: minutes) |
| --- | --- | --- |
| Degrees Celsius | Degrees Fahrenheit |  | Active Frost | Freezing Fog | Snow/ Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
| -3 and above | 27 and above | 100/0 | 8:00 | 1:30-3:05 | 0:30-1:00 | 0:55-1:35 | 0:40-0:50 | 0:15-1:10 |  |
|  |  | 75/25 | 5:00 | 1:40-3:30 | 0:30-1:05 | 0:45-1:15 | 0:40-0:50 | 0:15-1:40 |  |
|  |  | 50/50 | 3:00 | 1:00-2:10 | 0:15-0:30 | 0:15-0:25 | 0:05-0:15 | CAUTION: No holdover time guidelines exist |
| below -3 to -14 | below 27 to 7 | 100/0 | 8:00 | 0:35-1:25 | 0:25-0:45 | ***0:25-0:50 | ***0:10-0:30 |  |
|  |  | 75/25 | 5:00 | 0:35-1:15 | 0:25-0:50 | ***0:25-0:55 | ***0:15-0:30 |  |
| below -14 to -25 | below 7 to -13 | 100/0 | 8:00 | 0:20-0:45 | 0:15-0:30 |  |
| below -25 | below -13 | 100/0 | KILFROST ABC-2000 Type II fluid may be used below -25 °C (-13 °F) provided the freezing point of the fluid is at least 7 °C (13 °F) below the OAT and the aerodynamic acceptance criteria are met. Consider use of SAE Type I when KILFROST ABC-2000 Type II fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

* Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 °C (32 °F) only

*** No holdover time guidelines exist for this condition below  -10 (C (14 (F)

‡ Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- KILFROST ABC-2000 TYPE II FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT.

August 2006

## TABLE 2C - FAA Guideline for Holdover Times KILFROST ABC-TF2 Type II Fluid Mixtures as a Function of Weather Conditions and Outside Air Temperature

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Manufacturer Specific Type II Fluid Concentration Neat-Fluid/Water (Volume %/Volume %) | Approximate Holdover Times Under Various Weather Conditions (hours: minutes) |
| --- | --- | --- |
| Degrees Celsius | Degrees Fahrenheit |  | Active Frost | Freezing Fog | Snow/ Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
| -3 and above | 27 and above | 100/0 | 8:00 | 1:10-2:25 | 0:20-0:45 | 0:40-1:20 | 0:30-0:45 | 0:10-1:10 |  |
|  |  | 75/25 | 5:00 | 1:20-2:25 | 0:15-0:30 | 0:45-1:25 | 0:30-0:45 | 0:10-1:25 |  |
|  |  | 50/50 | 3:00 | 0:45-1:25 | 0:05-0:15 | 0:20-0:40 | 0:15-0:20 | CAUTION: No holdover time guidelines exist |
| below -3 to -14 | below 27 to 7 | 100/0 | 8:00 | 0:50-1:40 | 0:15-0:35 | ***0:35-1:15 | ***0:30-0:40 |  |
|  |  | 75/25 | 5:00 | 0:35-1:25 | 0:15-0:25 | ***0:30-1:30 | ***0:30-0:40 |  |
| below -14 to -25 | below 7 to -13 | 100/0 | 8:00 | 0:30-1:00 | 0:15-0:30 |  |
| below -25 | below -13 | 100/0 | KILFROST ABC-TF2 Type II fluid may be used below -25 °C (-13 °F) provided the freezing point of the fluid is at least 7 °C (13 °F) below the OAT and the aerodynamic acceptance criteria are met. Consider use of SAE Type I when KILFROST ABC-TF2 Type II fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

* Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 °C (32 °F) only

*** No holdover time guidelines exist for this condition below  -10 (C (14 (F)

‡ Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- KILFROST ABC-TF2 TYPE II FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT.

August 2006

TABLE 2D - FAA Guideline for Holdover Times OCTAGON E-MAX Type II Fluid Mixtures as a Function of Weather Conditions and Outside Air Temperature

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Manufacturer Specific Type II Fluid Concentration Neat-Fluid/Water (Volume %/Volume %) | Approximate Holdover Times Under Various Weather Conditions (hours: minutes) |
| --- | --- | --- |
| Degrees Celsius | Degrees Fahrenheit |  | Active Frost | Freezing Fog | Snow/ Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
| -3 and above | 27 and above | 100/0 | 8:00 | 2:05-3:45 | 0:40-1:20 | 0:45-1:35 | 0:30-0:40 | 0:15-1:30 |  |
|  |  | 75/25 | 5:00 | 1:25-2:50 | 0:25-0:55 | 0:40-1:10 | 0:20-0:30 | 0:10-1:05 |  |
|  |  | 50/50 | 3:00 | 0:30-0:55 | 0:10-0:25 | 0:15-0:30 | 0:10-0:15 | CAUTION: No holdover time guidelines exist |
| below -3 to -14 | below 27 to 7 | 100/0 | 8:00 | 0:50-1:45 | 0:35-1:10 | ***0:35-1:00 | ***0:20-0:30 |  |
|  |  | 75/25 | 5:00 | 0:30-1:20 | 0:25-0:50 | ***0:35-1:05 | ***0:15-0:30 |  |
| below -14 to -25 | below 7 to -13 | 100/0 | 8:00 | 0:20-0:35 | 0:15-0:30 |  |
| below -25 | below -13 | 100/0 | OCTAGON E-MAX Type II fluid may be used below -25 °C (-13 °F) provided the freezing point of the fluid is at least 7 °C (13 °F) below the OAT and the aerodynamic acceptance criteria are met. Consider use of SAE Type I when OCTAGON E-MAX Type II fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

* Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 °C (32 °F) only

*** No holdover time guidelines exist for this condition below  -10 (C (14 (F)

‡ Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- OCTAGON E-MAX TYPE II FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT.

August 2006

## TABLE 2E – FAA Guideline for Holdover Times SPCA ECOWING 26 Type II  Fluid Mixtures as a Function of Weather Conditions and Outside Air Temperature

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Manufacturer Specific Type II Fluid Concentration Neat-Fluid/Water (Volume %/Volume %) | Approximate Holdover Times Under Various Weather Conditions (hours: minutes) |
| --- | --- | --- |
| Degrees Celsius | Degrees Fahrenheit |  | Active Frost | Freezing Fog | Snow/ Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
| -3 and above | 27 and above | 100/0 | 8:00 | 1:25-2:35 | 0:40-1:00 | 0:50-1:35 | 0:40-0:50 | 0:20-1:25 |  |
|  |  | 75/25 | 5:00 | 1:05-1:55 | 0:25-0:45 | 0:45-1:05 | 0:25-0:35 | 0:10-1:00 |  |
|  |  | 50/50 | 3:00 | 0:30-0:45 | 0:10-0:20 | 0:15-0:25 | 0:05-0:10 | CAUTION: No holdover time guidelines exist |
| below -3 to -14 | below 27 to 7 | 100/0 | 8:00 | 0:45-2:15 | 0:35-0:55 | ***0:30-1:10 | ***0:15-0:35 |  |
|  |  | 75/25 | 5:00 | 0:35-1:15 | 0:25-0:40 | ***0:20-0:50 | ***0:15-0:25 |  |
| below -14 to -25 | below 7 to -13 | 100/0 | 8:00 | 0:25-0:45 | 0:15-0:30 |  |
| below -25 | below -13 | 100/0 | SPCA Ecowing 26 Type II fluid may be used below -25 °C (-13 °F) provided the freezing point of the fluid is at least 7 °C (13 °F) below the OAT and the aerodynamic acceptance criteria are met. Consider use of SAE Type I when SPCA Ecowing 26 Type II fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

* Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 °C (32 °F) only

*** No holdover time guidelines exist for this condition below  -10 (C (14 (F)

‡ Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- SPCA ECOWING 26 TYPE II FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT.

August 2006

## TABLE 2F – FAA Guideline for Holdover Times CLARIANT SAFEWING MP II 2025 ECO Type II Fluid Mixtures as a Function of Weather Conditions and Outside Air Temperature

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Manufacturer Specific Type II Fluid Concentration Neat-Fluid/Water (Volume %/Volume %) | Approximate Holdover Times Under Various Weather Conditions (hours: minutes) |
| --- | --- | --- |
| Degrees Celsius | Degrees Fahrenheit |  | Active Frost | Freezing Fog | Snow/Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
| -3 and above | 27 and above | 100/0 | 8:00 | 1:30-2:05 | 0:40-1:10 | 0:40-1:00 | 0:25-0:35 | 0:10-1:15 |  |
|  |  | 75/25 | 5:00 | 0:55-1:45 | 0:25-0:45 | 0:25-0:45 | 0:20-0:25 | 0:05-0:50 |  |
|  |  | 50/50 | 3:00 | 0:20-0:35 | 0:05-0:15 | 0:10-0:15 | 0:05-0:10 | CAUTION: No holdover time guidelines exist |
| below -3 to -14 | below 27 to 7 | 100/0 | 8:00 | 0:45-1:50 | 0:35-1:00 | ***0:35-1:05 | ***0:20-0:35 |  |
|  |  | 75/25 | 5:00 | 0:40-1:20 | 0:25-0:45 | ***0:30-0:40 | ***0:15-0:25 |  |
| below -14 to -25 | below 7 to -13 | 100/0 | 8:00 | 0:25-0:45 | 0:15-0:30 |  |
| below -25 | below -13 | 100/0 | CLARIANT Safewing mpii 2025 ECO Type II fluid may be used below -25 °C (-13 °F) provided the freezing point of the fluid is at least 7 °C (13 °F) below the OAT and the aerodynamic acceptance criteria are met. Consider use of SAE Type I when CLARIANT Safewing mpii 2025 Type II fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

* Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 °C (32 °F) only

*** No holdover time guidelines exist for this condition below  -10 (C (14 (F)

‡ Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- CLARIANT SAFEWING MP II 2025 ECO TYPE II FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT.

August 2006

## TABLE 2G – FAA Guideline for Holdover Times CLARIANT SAFEWING MP II Flight Type II Fluid Mixtures as a Function of Weather Conditions and Outside Air Temperature

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Manufacturer Specific Type II Fluid Concentration Neat-Fluid/Water (Volume %/Volume %) | Approximate Holdover Times Under Various Weather Conditions (hours: minutes) |
| --- | --- | --- |
| Degrees Celsius | Degrees Fahrenheit |  | Active Frost | Freezing Fog | Snow/Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
| -3 and above | 27 and above | 100/0 | 8:00 | 3:30-4:00 | 1:00-1:35 | 1:20-2:00 | 0:45-1:25 | 0:10-1:30 |  |
|  |  | 75/25 | 5:00 | 2:30-4:00 | 0:40-1:20 | 1:15-2:00 | 0:30-0:55 | 0:05-1:20 |  |
|  |  | 50/50 | 3:00 | 0:55-1:45 | 0:10-0:25 | 0:20-0:30 | 0:10-:015 | CAUTION: No holdover time guidelines exist |
| below -3 to -14 | below 27 to 7 | 100/0 | 8:00 | 0:55-1:45 | 0:40-1:05 | ***0:35-1:30 | ***0:25-0:45 |  |
|  |  | 75/25 | 5:00 | 0:40-1:10 | 0:20-0:40 | ***0:25-1:10 | ***0:30-0:40 |  |
| below -14 to -25 | below 7 to -13 | 100/0 | 8:00 | 0:30-0:50 | 0:15-0:30 |  |
| below -25 | below -13 | 100/0 | CLARIANT Safewing mp ii Flight Type II fluid may be used below -25 °C (-13 °F) provided the freezing point of the fluid is at least 7 °C (13 °F) below the OAT and the aerodynamic acceptance criteria are met. Consider use of SAE Type I when CLARIANT Safewing mp ii Flight Type II fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

* Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 °C (32 °F) only

*** No holdover time guidelines exist for this condition below  -10 (C (14 (F)

‡ Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- CLARIANT SAFEWING MP II FLIGHT TYPE II FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT.

August 2006

### FAA TYPE III  Holdover Time Guideline

### Table 3.   FAA Guideline for Holdover Times SAE Type III Fluid Mixture as a Function of Weather Conditions and OAT.

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRETAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Approximate Holdover Times Under Various Weather Conditions (hours: minutes) |
| --- | --- |
| Degrees Celsius | Degrees Fahrenheit | Type III Fluid Concentration Neat Fluid/Water (Volume %/Volume %) | Active Frost | Freezing Fog | Snow/Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
|  |  |  |  |  | Very Light | Light | Moderate |  |  |  |  |
| -3 and above | 27 and above | 100/0 | 2:00 | 0:20 - 0:40 | 0:35 - 0:40 | 0:20 - 0:35 | 0:10 - 0:20 | 0:10 - 0:20 | 0:08 - 0:10 | 0:06 - 0:20 |  |
|  |  | 75/25 | 1:00 | 0:15 - 0:30 | 0:25 - 0:35 | 0:15 - 0:25 | 0:08 - 0:15 | 0:08 - 0:15 | 0:06 - 0:10 | 0:02 - 0.10 |  |
|  |  | 50/50 | 0:30 | 0:10 - 0:20 | 0:15 - 0:20 | 0:08 - 0:15 | 0:04 - 0:08 | 0:05 - 0:09 | 0:04 - 0:06 |  |  |
| below -3 to -10 | below 27 to 21 | 100/0 | 2:00 | 0:20 - 0: 40 | 0:30 - 0:35 | 0:15 - 0:30 | 0:09 - 0:15 | 0:10 - 0:20 | 0:08 - 0:10 |  |
|  |  | 75/25 | 1:00 | 0:15 - 0:30 | 0:25 - 0:30 | 0:10 - 0:25 | 0:07 - 0:10 | 0:09 - 0:12 | 0:06 - 0:09 |  |
| below -10 | below 14 | 100/0 | 2:00 | 0:20 - 0:40 | 0:30 - 0:35 | 0:15 - 0:30 | 0:08 - 0:15 | CAUTION: No holdover time guidelines exist |
| SAE Type III fluid may be used below -10(C (14(F), provided the freezing point of the fluid is at least 7(C (13(F) below OAT and aerodynamic acceptance criteria are met. Consider the use of SAE Type I when Type III fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

*Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

**This column is for use at temperatures above 0 °C (32 °F) only

‡Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST WILL REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- SAE TYPE III FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR - AND DOES NOT PROVIDE - PROTECTION DURING FLIGHT.

August 2006

FAA TYPE IV Holdover Time Guideline

## TABLE 4 - FAA Guideline for Holdover Times SAE Type IV Fluid Mixtures as a Function of Weather Conditions and OAT.

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Type IV Fluid Concentration Neat-Fluid/Water (Volume %/Volume %) | Approximate Holdover Times Under Various Weather Conditions (hours: minutes) |
| --- | --- | --- |
| Degrees Celsius | Degrees Fahrenheit |  | Active Frost | Freezing Fog | Snow/Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
| -3 and above | 27 and above | 100/0 | 12:00 | 1:15-2:30 | 0:35-1:15 | 0:40-1:10 | 0:25-0:40 | 0:10-0:50 |  |
|  |  | 75/25 | 5:00 | 1:05-1:45 | 0:20-0:55 | 0:35-0:50 | 0:15-0:30 | 0:05-0:35 |  |
|  |  | 50/50 | 3:00 | 0:15-0:35 | 0:05-0:15 | 0:10-0:20 | 0:05-0:10 | CAUTION: No holdover time guidelines exist |
| below -3 to -14 | below 27 to 7 | 100/0 | 12:00 | 0:20-1:20 | 0:20-0:40 | ***0:20-0:45 | ***0:10-0:25 |  |
|  |  | 75/25 | 5:00 | 0:25-0:50 | 0:15-0:35 | ***0:15-0:30 | ***0:10-0:20 |  |
| below -14 to -25 | below 7 to -13 | 100/0 | 12:00 | 0:15-0:40 | 0:15-0:30 |  |
| below -25 | below -13 | 100/0 | SAE Type IV fluid may be used below -25 °C (-13 °F) provided the freezing point of the fluid is at least 7 °C(13 °F) below the OAT and the aerodynamic acceptance criteria are met. Consider use of SAE Type I when SAE Type IV fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

*  Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 °C (32°F) only

*** No holdover time guidelines exist for this condition below  -10 (C (14 (F)

‡ Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- SAE TYPE IV FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT.

August 2006

## TABLE 4A - FAA Guideline for Holdover Times DOW UCAR ULTRA+ Type IV Fluid Mixtures as a Function of Weather Conditions and Outside Air Temperature

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Manufacturer Specific Type IV Fluid Concentration Neat-Fluid/Water (Volume %/Volume %) | Approximate Holdover Times Under Various Weather Contions (hours: minutes) |
| --- | --- | --- |
| Degrees Celsius | Degrees Fahrenheit |  | Active Frost | Freezing Fog | Snow/ Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
| -3 and above | 27 and above | 100/0 | 12:00 | 1:35-3:35 | 0:35-1:15 | 0:45-1:35 | 0:25-0:40 | 0:10-1:20 |  |
|  |  | 75/25 |  |  |  |  |  | CAUTION: No holdover time guidelines exist |
|  |  | 50/50 |  |  |  |  |  |  |
| below -3 to -14 | below 27 to 7 | 100/0 | 12:00 | 1:25-3:00 | 0:25-0:55 | ***0:45-1:25 | ***0:30-0:45 |  |
|  |  | 75/25 |  |  |  |  |  |  |
| below -14 to -24 | below 7 to -12 | 100/0 | 12:00 | 0:40-2:10 | 0:20-0:45 |  |
| below -24 | below -12 | 100/0 | DOW UCAR ULTRA+ Type IV fluid may be used below -24 °C (-12 °F) provided the freezing point of the fluid is at least 7 °C (13 °F) below the OAT and the aerodynamic acceptance criteria are met. Consider use of SAE Type I when DOW UCAR ULTRA+ Type IV fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

* Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 °C (32 °F) only

*** No holdover time guidelines exist for this condition below  -10 (C (14 (F)

‡ Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- DOW UCAR ULTRA+ TYPE IV FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT.

August 2006

## TABLE 4B - 	FAA Guideline for Holdover Times DOW UCAR ENDURANCE EG106 Type IV Fluid Mixtures as a Function of Weather Conditions and Outside Air Temperature

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Manufacturer Specific Type IV Fluid Concentration Neat-Fluid/Water (Volume %/Volume %) | Approximate Holdover Times Under Various Weather Contions (hours: minutes) |
| --- | --- | --- |
| Degrees Celsius | Degrees Fahrenheit |  | Active Frost | Freezing Fog | Snow/ Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
| -3 and above | 27 and above | 100/0 | 12:00 | 2:05-3:10 | 0:40-1:20 | 1:10-2:00 | 0:50-1:15 | 0:10-1:20 |  |
|  |  | 75/25 |  |  |  |  |  | CAUTION: No holdover time guidelines exist |
|  |  | 50/50 |  |  |  |  |  |  |
| below -3 to -14 | below 27 to 7 | 100/0 | 12:00 | 1:50-3:20 | 0:30-1:05 | ***0:55-1:50 | ***0:45-1:10 |  |
|  |  | 75/25 |  |  |  |  |  |  |
| below -14 to -24 | below 7 to -12 | 100/0 | 12:00 | 0:30-1:05 | 0:15-0:30 |  |
| below -24 | below -12 | 100/0 | DOW UCAR ENDURANCE EG 106 Type IV fluid may be used below -25 °C (-13 °F) provided the freezing point of the fluid is at least 7 °C (13 °F) below the OAT and the aerodynamic acceptance criteria are met. Consider use of SAE Type I when DOW UCAR ENDURANCE EG 106 Type IV fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

* Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 °C (32 °F) only

*** No holdover time guidelines exist for this condition below  -10 (C (14 (F)

‡ Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- DOW UCAR ENDURANCE EG 106 TYPE IV FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT.

August 2006

TABLE 4C - FAA Guideline for Holdover Times DOW UCAR FLIGHTGUARD AD-480 Type IV Fluid Mixtures as a function of Weather	 Conditions and Outside Air Temperature

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Manufacturer Specific Type IV Fluid Concentration Neat-Fluid/Water (Volume %/Volume %) | Approximate Holdover Times Under Various Weather Conditions (hours: minutes) |
| --- | --- | --- |
| Degrees Celsius | Degrees Fahrenheit |  | Active Frost | Freezing Fog | Snow/ Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
| -3 and above | 27 and above | 100/0 | 12:00 | 2:00-3:30 | 0:40-1:20 | 0:50-1:30 | 0:35-0:55 | 0:15-1:35 |  |
|  |  | 75/25 | 5:00 | 1:30-2:45 | 0:30-1:05 | 0:50-1:15 | 0:30-0:45 | 0:10-1:15 |  |
|  |  | 50/50 | 3:00 | 0:30-0:45 | 0:10-0:20 | 0:15-0:25 | 0:05-0:15 | CAUTION: No holdover time guidelines exist |
| below -3 to -14 | below 27 to 7 | 100/0 | 12:00 | 0:20-1:20 | 0:30-0:55 | ***0:25-1:20 | ***0:15-0:30 |  |
|  |  | 75/25 | 5:00 | 0:25-0:50 | 0:20-0:45 | ***0:25-1:05 | ***0:15-0:30 |  |
| below -14 to -25 | below 7 to -13 | 100/0 | 12:00 | 0:15-0:40 | 0:15-0:30 |  |
| below -25 | below -13 | 100/0 | DOW UCAR FLIGHTGUARD AD-480 Type IV fluid may be used below -25 °C (-13 °F) provided the freezing point of the fluid is at least 7 °C (13 °F) below the OAT and the aerodynamic acceptance criteria are met. Consider use of SAE Type I when DOW UCAR FLIGHTGUARD AD-480 Type IV fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

* Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 degrees Celsius (32 degrees Fahrenheit) only

*** No holdover time guidelines exist for this condition below  -10 (C (14 (F)

‡ Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- DOW UCAR FLIGHTGUARD AD-480 TYPE IV FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT.

## August 2006

## TABLE 4D - FAA Guideline for Holdover Times OCTAGON MAX-FLIGHT Type IV Fluid Mixtures as a Function of Weather Conditions and Outside Air Temperature

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Manufacturer Specific Type IV Fluid Concentration Neat-Fluid/Water (Volume %/Volume %) | Approximate Holdover Times Under Various Weather Conditions (hours: minutes) |
| --- | --- | --- |
| Degrees Celsius | Degrees Fahrenheit |  | Active Frost | Freezing Fog | Snow/Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
| -3 and above | 27 and above | 100/0 | 12:00 | 2:40-4:00 | 0:50-1:35 | 0:55-2:00 | 0:35-1:00 | 0:15-1:15 |  |
|  |  | 75/25 | 5:00 | 2:05-3:15 | 0:45-1:45 | 1:15-2:00 | 0:35-1:10 | 0:10-0:40 |  |
|  |  | 50/50 | 3:00 | 0:55-1:45 | 0:25-1:15 | 0:35-1:00 | 0:15-0:30 | CAUTION: No holdover time guidelines exist |
| below -3 to -14 | below 27 to 7 | 100/0 | 12:00 | 0:50-2:30 | 0:25-0:50 | ***0:25-1:10 | ***0:20-0:40 |  |
|  |  | 75/25 | 5:00 | 0:30-1:05 | 0:20-0:50 | ***0:20-1:00 | ***0:15-0:30 |  |
| below -14 to -25 | below 7 to -13 | 100/0 | 12:00 | 0:20-0:45 | 0:15-0:30 |  |
| below -25 | below -13 | 100/0 | OCTAGON MAX-FLIGHT Type IV fluid may be used below -25 °C (-13 °F) provided the freezing point of the fluid is at least 7 °C (13 °F) below the OAT and the aerodynamic acceptance criteria are met. Consider use of SAE Type I when OCTAGON MAX-FLIGHT Type IV fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

* Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 °C (32 °F) only

*** No holdover time guidelines exist for this condition below  -10 (C (14 (F)

‡ Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- OCTAGON MAX-FLIGHT TYPE IV FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT.

August, 2006

## TABLE 4E - FAA Guideline for Holdover Times OCTAGON MAX-FLIGHT 04 Type IV Fluid Mixtures as a Function of Weather Conditions and Outside Air Temperature

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Manufacturer Specific Type IV Fluid Concentration Fluid/Water (Volume %/Volume %) | Approximate Holdover Times Under Various Weather Conditions (hours: minutes) |
| --- | --- | --- |
| Degrees Celsius | Degrees Fahrenheit |  | Active Frost | Freezing Fog | Snow/Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
| -3 and above | 27 and above | 100/0 | 12:00 | 2:40-4:00 | 1:25-2:00 | 2:00-2:00 | 1:10-1:30 | 0:20-2:00 |  |
|  |  | 75/25 | 5:00 | 2:05-3:15 | 1:05-2:00 | 1:50-2:00 | 1:00-1:20 | 0:20-2:00 |  |
|  |  | 50/50 | 3:00 | 0:55-1:45 | 0:25-1:15 | 0:35-1:10 | 0:25-0:35 | CAUTION: No holdover time guidelines exist |
| below -3 to -14 | below 27 to 7 | 100/0 | 12:00 | 0:50-2:30 | 0:35-1:10 | ***0:25-1:30 | ***0:20-0:40 |  |
|  |  | 75/25 | 5:00 | 0:30-1:05 | 0:40-1:20 | ***0:20-1:00 | ***0:15-0:30 |  |
| below -14 to -25 | below 7 to -13 | 100/0 | 12:00 | 0:20-0:45 | 0:15-0:30 |  |
| below -25 | below -13 | 100/0 | OCTAGON MAX-FLIGHT 04 Type IV fluid may be used below -25 °C (-13 °F) provided the freezing point of the fluid is at least 7 °C (13 °F) below the OAT and the aerodynamic acceptance criteria are met. Consider use of SAE Type I when OCTAGON MAX-FLIGHT 04 Type IV fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

* Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 °C (32 °F) only

*** No holdover time guidelines exist for this condition below  -10 (C (14 (F)

‡ Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- OCTAGON MAX-FLIGHT 04 TYPE IV FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT.
																     August 2006

## TABLE 4F - FAA Guideline for Holdover Times OCTAGON MAXFLO Type IV Fluid Mixtures as a Function of Weather Conditions and Outside Air Temperature

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Manufacturer Specific Type IV Fluid Concentration Neat-Fluid/Water (Volume %/Volume %) | Approximate Holdover Times Under Various Weather Conditions (hours: minutes) |
| --- | --- | --- |
| Degrees Celsius | Degrees Fahrenheit |  | Frost | Freezing Fog | Snow /Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
| -3 and above | 27 and above | 100/0 | 12:00 | 2:20-3:35 | 0:40-1:30 | 1:20-2:00 | 0:30-1:00 | 0:10-2:00 |  |
|  |  | 75/25 | 5:00 | 1:25-2:00 | 0:20-0:55 | 0:40-1:05 | 0:20-0:35 | 0:05-1:15 |  |
|  |  | 50/50 | 3:00 | 0:20-0:40 | 0:05-0:15 | 0:10-0:20 | 0:05-0:10 | CAUTION: No holdover time guidelines exist |
| below -3 to -14 | below 27 to 7 | 100/0 | 12:00 | 1:10-2:20 | 0:25-1:00 | ***0:35-1:45 | ***0:30-0:50 |  |
|  |  | 75/25 | 5:00 | 0:40-1:25 | 0:15-0:40 | ***0:35-1:15 | ***0:15-0:30 |  |
| below -14 to -25 | below 7 to -13 | 100/0 | 12:00 | 0:30-1:00 | 0:15-0:30 |  |
| below -25 | below -13 | 100/0 | OCTAGON MAXFLO Type IV fluid may be used below -25 °C (-13 °F) provided the freezing point of the fluid is at least 7 °C (13 °F) below the OAT and the aerodynamic acceptance criteria are met. Consider use of SAE Type I when OCTAGON MAXFLO Type IV fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

* Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 °C (32 °F) only

*** No holdover time guidelines exist for this condition below  -10 (C (14 (F)

‡ Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- OCTAGON MAXFLO TYPE IV FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT.

August 2006

## TABLE 4G - FAA Guideline for Holdover Times KILFROST ABC-S Type IV Fluid Mixtures as a Function of Weather Conditions and Outside Air Temperature

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Manufacturer Specific Type IV Fluid Concentration Fluid/Water (Volume %/Volume %) | Approximate Holdover Times Under Various Weather Conditions (hours: minutes) |
| --- | --- | --- |
| Degrees Celsius | Degrees Fahrenheit |  | Active Frost | Freezing Fog | Snow/ Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
| -3 and above | 27 and above | 100/0 | 12:00 | 2:35-4:00 | 1:00-1:40 | 1:20-1:50 | 1:00-1:25 | 0:20-1:15 |  |
|  |  | 75/25 | 5:00 | 1:05-1:45 | 0:30-0:55 | 0:45-1:10 | 0:35-0:50 | 0:10-0:50 |  |
|  |  | 50/50 | 3:00 | 0:20-0:35 | 0:05-0:15 | 0:15-0:20 | 0:05-0:10 | CAUTION: No holdover time guidelines exist |
| below -3 to -14 | below 27 to 7 | 100/0 | 12:00 | 0:45-2:05 | 0:45-1:20 | ***0:20-1:00 | ***0:10-0:30 |  |
|  |  | 75/25 | 5:00 | 0:25-1:00 | 0:25-0:50 | ***0:20-1:10 | ***0:10-0:35 |  |
| below -14 to -25 | below 7 to -13 | 100/0 | 12:00 | 0:20-0:40 | 0:15-0:30 |  |
| below -25 | below -13 | 100/0 | KILFROST ABC-S Type IV fluid may be used below -25 °C (-13 °F) provided the freezing point of the fluid is at least 7 °C (13 °F) below the OAT and the aerodynamic acceptance criteria are met. Consider use of SAE Type I when KILFROST ABC-S Type IV fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

* Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 degrees Celsius (32 degrees Fahrenheit) only

*** No holdover time guidelines exist for this condition below  -10 (C (14 (F)

‡ Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- KILFROST ABC-S TYPE IV FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT.

August 2006

## TABLE 4H - FAA Guideline for Holdover Times KILFROST ABC-S PLUS Type IV Fluid Mixtures as a Function of Weather Conditions and Outside Air Temperature

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Manufacturer Specific Type IV Fluid Concentration Fluid/Water (Volume %/Volume %) | Approximate Holdover Times Under Various Weather Conditions (hours: minutes) |
| --- | --- | --- |
| Degrees Celsius | Degrees Fahrenheit |  | Active Frost | Freezing Fog | Snow/ Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
| -3 and above | 27 and above | 100/0 | 12:00 | 1:50-3:40 | 0:45-1:25 | 1:15-1:55 | 0:50-1:10 | 0:15-1:40 |  |
|  |  | 75/25 | 5:00 | 1:10-2:10 | 0:25-0:55 | 0:45-1:10 | 0:30-0:45 | 0:05-1:00 |  |
|  |  | 50/50 | 3:00 | 0:20-0:40 | 0:05-0:15 | 0:10-0:20 | 0:05-0:10 | CAUTION: No holdover time guidelines exist |
| below -3 to -14 | below 27 to 7 | 100/0 | 12:00 | 0:40-1:25 | 0:35-1:0 0 | ***0:30-1:35 | ***0:25-0:35 |  |
|  |  | 75/25 | 5:00 | 0:40-1:15 | 0:25-0:50 | ***0:25-1:15 | ***0:30-0:40 |  |
| below -14 to -25 | below 7 to -13 | 100/0 | 12:00 | 0:20-0:45 | 0:15-0:30 |  |
| below -25 | below -13 | 100/0 | KILFROST ABC-S PLUS Type IV fluid may be used below -25 °C (-13 °F) provided the freezing point of the fluid is at least 7 °C (13 °F) below the OAT and the aerodynamic acceptance criteria are met. Consider use of SAE Type I when KILFROST ABC-S PLUS Type IV fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

* Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 degrees Celsius (32 degrees Fahrenheit) only

*** No holdover time guidelines exist for this condition below -10 (C (14 (F)

‡ Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- KILFROST ABC-S PLUS TYPE IV FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT.

                                                                                                                                                                                                                                                                         August 2006

## TABLE 4I – FAA Guideline for Holdover Times CLARIANT SAFEWING MP IV  2001 Type IV Fluid Mixtures as a Function of Weather Conditions and Outside Air Temperature

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Manufacturer Specific Type IV Fluid Concentration Neat-Fluid/Water (Volume %/Volume %) | Approximate Holdover Times Under Various Weather Conditions (hours: minutes) |
| --- | --- | --- |
| Degrees Celsius | Degrees Fahrenheit |  | Active Frost | Freezing Fog | Snow/ Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
| -3 and above | 27 and above | 100/0 | 12:00 | 1:20-3:20 | 1:00-1:55 | 0:55-1:55 | 0:40-1:00 | 0:15-2:00 |  |
|  |  | 75/25 | 5:00 | 1:20-2:00 | 0:35-1:00 | 0:35-1:10 | 0:25-0:35 | 0:10-1:25 |  |
|  |  | 50/50 | 3:00 | 0:15-0:40 | 0:10-0:20 | 0:10-0:20 | 0:05-0:15 | CAUTION: No holdover time guidelines exist |
| below -3 to -14 | below 27 to 7 | 100/0 | 12:00 | 0:45-1:35 | 0:30-0:50 | ***0:55-1:35 | ***0:30-0:45 |  |
|  |  | 75/25 | 5:00 | 0:30-1:00 | 0:20-0:35 | ***0:40-1:10 | ***0:20-0:30 |  |
| below -14 to -25 | below 7 to -13 | 100/0 | 12:00 | 0:20-0:45 | 0:15-0:30 |  |
| below -25 | below -13 | 100/0 | CLARIANT SAFEWING MP IV 2001 Type IV fluid may be used below -25 °C (-13 °F) provided the freezing point of the fluid is at least 7 °C (13 °F) below the OAT and the aerodynamic acceptance criteria are met. Consider use of SAE Type I when CLARIANT SAFEWING MP IV 2001 Type IV fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

* Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 °C (32 °F) only

*** No holdover time guidelines exist for this condition below  -10 (C (14 (F)

‡ Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- CLARIANT SAFEWING MP IV 2001 TYPE IV FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT.

August 2006

## TABLE 4J – FAA Guideline for Holdover Times CLARIANT SAFEWING MP IV 2012 PROTECT Type IV Fluid Mixtures as a Function of Weather Conditions and Outside Air Temperature

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Manufacturer Specific Type IV Fluid Concentration Neat-Fluid/Water (Volume %/Volume %) | Approximate Holdover Times Under Various Weather Conditions (hours: minutes) |
| --- | --- | --- |
| Degrees Celsius | Degrees Fahrenheit |  | Active Frost | Freezing Fog | Snow/ Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
| -3 and above | 27 and above | 100/0 | 12:00 | 1:15-2:30 | 0:40-1:15 | 0:40-1:10 | 0:25-0:45 | 0:10-1:05 |  |
|  |  | 75/25 | 5:00 | 1:10-2:05 | 0:25-0:55 | 0:35-0:50 | 0:15-0:30 | 0:05-0:40 |  |
|  |  | 50/50 | 3:00 | 0:25-0:45 | 0:15-0:25 | 0:15-0:20 | 0:05-0:10 | CAUTION: No holdover time guidelines exist |
| below -3 to -14 | below 27 to 7 | 100/0 | 12:00 | 0:45-1:45 | 0:20-0:40 | ***0:25-0:45 | ***0:15-0:25 |  |
|  |  | 75/25 | 5:00 | 0:25-1:05 | 0:20-0:40 | ***0:15-0:30 | ***0:10-0:20 |  |
| below -14 to -25 | below 7 to -13 | 100/0 | 12:00 | 0:20-0:45 | 0:15-0:30 |  |
| below -25 | below -13 | 100/0 | CLARIANT SAFEWING MP IV 2012 PROTECT Type IV fluid may be used below -25 °C (-13 °F) provided the freezing point of the fluid is at least 7 °C (13 °F) below the OAT and the aerodynamic acceptance criteria are met. Consider use of SAE Type I when CLARIANT SAFEWING MP IV 2012 PROTECT Type IV fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

* Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 °C (32 °F) only

*** No holdover time guidelines exist for this condition below -10 (C (14 (F)

‡ Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- CLARIANT SAFEWING MP IV 2012 PROTECT TYPE IV FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT.

August 2006

## TABLE 4K - FAA Guideline for Holdover Times CLARIANT SAFEWING MP IV 2030 ECO Type IV Fluid Mixtures as a function of Weather Conditions and Outside Air Temperature

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Manufacturer Specific Type IV Fluid Concentration Neat-Fluid/Water (Volume %/Volume %) | Approximate Holdover Times Under Various Weather Conditions (hours: minutes) |
| --- | --- | --- |
| Degrees Celsius | Degrees Fahrenheit |  | Active Frost | Freezing Fog | Snow/ Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
| -3 and above | 27 and above | 100/0 | 12:00 | 1:55-3:20 | 0:50-1:30 | 0:55-2:00 | 0:40-0:50 | 0:15-1:40 |  |
|  |  | 75/25 | 5:00 | 1:15-2:05 | 0:35-1:05 | 0:40-1:05 | 0:25-0:35 | 0:10-1:00 |  |
|  |  | 50/50 | 3:00 | 0:30-0:45 | 0:15-0:25 | 0:15-0:25 | 0:05-0:10 | CAUTION: No holdover time guidelines exist |
| below -3 to -14 | below 27 to 7 | 100/0 | 12:00 | 0:50-2:00 | 0:45-1:25 | ***0:30-1:10 | ***0:20-0:35 |  |
|  |  | 75/25 | 5:00 | 0:40-1:30 | 0:35-1:05 | ***0:35-1:20 | ***0:15-0:30 |  |
| below -14 to -25 | below 7 to -13 | 100/0 | 12:00 | 0:25-0:45 | 0:15-0:30 |  |
| below -25 | below -13 | 100/0 | CLARIANT SAFEWING MPIV 2030 ECO Type IV fluid may be used below -25 °C (-13 °F) provided the freezing point of the fluid is at least 7 °C (13 °F) below the OAT and the aerodynamic acceptance criteria are met. Consider use of SAE Type I when CLARIANT SAFEWING MPIV 2030 ECO Type IV fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

* Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 degrees Celsius (32 degrees Fahrenheit) only

*** No holdover time guidelines exist for this condition below  -10 (C (14 (F)

‡ Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- CLARIANT SAFEWING MP IV 2030 ECO TYPE IV FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT

August 2006

## TABLE 4L - FAA Guideline for Holdover Times CLARIANT SAFEWING MP IV LAUNCH Type IV Fluid Mixtures as a function of Weather Conditions and Outside Air Temperature

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Manufacturer Specific Type IV Fluid Concentration Neat-Fluid/Water (Volume %/Volume %) | Approximate Holdover Times Under Various Weather Conditions (hours: minutes) |
| --- | --- | --- |
| Degrees Celsius | Degrees Fahrenheit |  | Active Frost | Freezing Fog | Snow/ Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
| -3 and above | 27 and above | 100/0 | 12:00 | 4:00-4:00 | 1:00-1:35 | 1:30-2:00 | 1:00-1:40 | 0:15-1:40 |  |
|  |  | 75/25 | 5:00 | 3:40-4:00 | 0:40-1:20 | 1:40-2:00 | 0:45-1:15 | 0:10-1:45 |  |
|  |  | 50/50 | 3:00 | 1:25-2:45 | 0:10-0:25 | 0:30-0:50 | 0:20-0:25 | CAUTION: No holdover time guidelines exist |
| below -3 to -14 | below 27 to 7 | 100/0 | 12:00 | 1:00-1:55 | 0:40-1:05 | ***0:35-1:40 | ***0:25-0:45 |  |
|  |  | 75/25 | 5:00 | 0:40-1:20 | 0:20-0:40 | ***0:25-1:10 | ***0:25-0:45 |  |
| below -14 to -25 | below 7 to -13 | 100/0 | 12:00 | 0:30-0:50 | 0:15-0:30 |  |
| below -25 | below -13 | 100/0 | CLARIANT SAFEWING MPIV LAUNCH Type IV fluid may be used below -25 °C (-13 °F) provided the freezing point of the fluid is at least 7 °C (13 °F) below the OAT and the aerodynamic acceptance criteria are met. Consider use of SAE Type I when CLARIANT SAFEWING MPIV LAUNCH Type IV fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

* Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 degrees Celsius (32 degrees Fahrenheit) only

*** No holdover time guidelines exist for this condition below  -10 (C (14 (F)

‡ Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- CLARIANT SAFEWING MP IV LAUNCH TYPE IV FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT

August  2006

TABLE 4M - FAA Guideline for Holdover Times SPCA AD-480 Type IV Fluid Mixtures as a function of Weather Conditions and Outside Air Temperature

CAUTION:  THIS TABLE IS FOR DEPARTURE PLANNING ONLY AND SHOULD BE USED IN CONJUNCTION WITH PRE-TAKEOFF CHECK PROCEDURES.

| Outside Air Temperature | Manufacturer Specific Type IV Fluid Concentration Neat-Fluid/Water (Volume %/Volume %) | Approximate Holdover Times Under Various Weather Conditions (hours: minutes) |
| --- | --- | --- |
| Degrees Celsius | Degrees Fahrenheit |  | Active Frost | Freezing Fog | Snow/ Snow Grains | Freezing Drizzle* | Light Freezing Rain | Rain on Cold Soaked Wing** | Other‡ |
| -3 and above | 27 and above | 100/0 | 12:00 | 2:00-3:30 | 0:40-1:20 | 0:50-1:30 | 0:35-0:55 | 0:15-1:35 |  |
|  |  | 75/25 | 5:00 | 1:30-2:45 | 0:30-1:05 | 0:50-1:15 | 0:30-0:45 | 0:10-1:15 |  |
|  |  | 50/50 | 3:00 | 0:30-0:45 | 0:10-0:20 | 0:15-0:25 | 0:05-0:15 | CAUTION: No holdover time guidelines exist |
| below -3 to -14 | below 27 to 7 | 100/0 | 12:00 | 0:20-1:20 | 0:30-0:55 | ***0:25-1:20 | ***0:15-0:30 |  |
|  |  | 75/25 | 5:00 | 0:25-0:50 | 0:20-0:45 | ***0:25-1:05 | ***0:15-0:30 |  |
| below -14 to -25 | below 7 to -13 | 100/0 | 12:00 | 0:15-0:40 | 0:15-0:30 |  |
| below -25 | below -13 | 100/0 | SPCA AD-480 Type IV fluid may be used below -25 °C (-13 °F) provided the freezing point of the fluid is at least 7 °C (13 °F) below the OAT and the aerodynamic acceptance criteria are met. Consider use of SAE Type I when SPCA AD-480 Type IV fluid cannot be used. |

THE RESPONSIBILITY FOR THE APPLICATION OF THESE DATA REMAINS WITH THE USER.

* Use light freezing rain holdover times if positive identification of freezing drizzle is not possible

** This column is for use at temperatures above 0 degrees Celsius (32 degrees Fahrenheit) only

*** No holdover time guidelines exist for this condition below  -10 (C (14 (F)

‡ Snow pellets, ice pellets, heavy snow, moderate and heavy freezing rain, and hail

CAUTIONS:

- THE TIME OF PROTECTION WILL BE SHORTENED IN HEAVY WEATHER CONDITIONS.  HEAVY PRECIPITATION RATES OR HIGH MOISTURE CONTENT, HIGH WIND VELOCITY, OR JET BLAST MAY REDUCE HOLDOVER TIME BELOW THE LOWEST TIME STATED IN THE RANGE.  HOLDOVER TIME MAY BE REDUCED WHEN AIRCRAFT SKIN TEMPERATURE IS LOWER THAN OAT.

- SPCA AD-480 TYPE IV FLUID USED DURING GROUND DEICING/ANTI-ICING IS NOT INTENDED FOR AND DOES NOT PROVIDE PROTECTION DURING FLIGHT.

August 2006

TABLE 5 - FAA Guidelines for the Application of SAE Type II, Type III and Type IV Fluid Mixtures. Minimum Concentrations as a Function of Outside Air Temperature (OAT).

Concentrations in % Volume

| OAT | One-step Procedure Deicing/Anti-icing | Two-step Procedure |
| --- | --- | --- |
|  |  | First step: Deicing | Second step: Anti-icing1, 2, 3 |
| -3 (C (27 (F) and above | 50/50 Heated 2 Type II, III or IV | Heated water or a heated mix of Type I, II, III or IV and water | 50/50 Type II, III, or IV |
| Below -3 (C (27 (F) to -14 (C (7 (F) | 75/25 Heated 2 Type II, III or IV | Heated suitable mix of Type I, II, III or IV, and water with a freezing point not more than 3 (C (5 (F) above actual OAT | 75/25 Type II, III, or IV |
| below -14 (C (7 (F) to -25 (C (-13 (F) | 100/0 Heated 2 Type II, III or IV | Heated suitable mix of Type I, II, III or IV, and water with a freezing point not more than 3 (C (5 (F) above actual OAT | 100/0 Type II, III, or IV |
| Below -25 (C (-13 (F) | SAE Type II/IV fluid may be used below -25 (C (-13 (F) provided that the freezing point of the fluid is at least a 7 (C (13 (F) below OAT and that aerodynamic acceptance criteria are met. SAE Type III fluid may be used below -10 (C (14 (F) provided that the freezing point of the fluid is at least 7(C (13 (F) below OAT and that aerodynamic acceptance criteria are met. Consider the use of SAE Type I when Type II, III or IV fluid cannot be used. |
| 1) Fluids must only be used at temperatures above their lowest operational use temperature. 2) To be applied before first step fluid freezes, typically within 3 minutes. 3) Clean aircraft may be anti-iced with unheated Type II, III, or IV fluid. |
| NOTE: For heated fluids, a fluid temperature not less than 60 (C (140 (F) at the nozzle is desirable. Upper temperature limit shall not exceed fluid and aircraft manufacturers’ recommendations. |
| CAUTIONS: Wing skin temperatures may differ and, in some cases, be lower than OAT. A stronger mix (more glycol) can be used under these conditions. As fluid freezing may occur, 50/50 Type II, III, or IV fluid shall not be used for the anti-icing step of a cold-soaked wing as indicated by frost or ice on the lower surface of the wing in the area of the fuel tank. An insufficient amount of anti-icing fluid, especially in the second step of a two-step procedure, may cause a substantial loss of holdover time, particularly when using a Type I fluid mixture for the first step (deicing) of a two-step procedure. |

August 2006

TABLE 6.  LOWEST ON-WING VISCOSITY VALUES FOR NEAT SAE TYPE II AND TYPE IV FLUIDS

|  | Fluid Name | Lowest On-Wing Viscosity a (mPa.s) |
| --- | --- | --- |
|  |  | Manufacturer Method | SAE AIR 9968 revision a method |
| Type II | Clariant Safewing MP II 2025 ECO | 5,500 b | 5,750 g |
|  | Clariant Safewing MP II Flight | 3,340 g | 3,340 g |
|  | Kilfrost ABC-2000 | 2,350 c | 2,350 g |
|  | Kilfrost ABC-II Plus | 3,600 c | 3,600 g |
|  | Kilfrost ABC-TF2 | 3,550 c | 3,460 g |
|  | Octagon E Max | 13,520 d | 13,520 g |
|  | SPCA Ecowing 26 | 4,900 e | 4,600 g |
| Type IV | Clariant Safewing MP IV 2001 | 18,000 b | 18,000 c |
|  | Clariant Safewing MP IV 2012 Protect | 7,800 b | 7,250 g |
|  | Clariant Safewing MP IV 2030 ECO | 10,500 b | 10,500 c |
|  | Clariant Safewing MP IV Launch | 7,550 g | 7,550 g |
|  | Dow UCAR AAF ULTRA+ | 36,000 f | 28,000 c |
|  | Dow UCAR Endurance EG 106 | 24,850 f | 2,230 g |
|  | Dow UCAR AD-480 | 15,200 e | 12,800 c |
|  | Kilfrost ABC-S | 17,000 c | 17,000 c |
|  | Kilfrost ABC-S PLUS | 10,450 c | 11,040 g |
|  | Octagon Max-Flight | 5,540 d | 5,540 g |
|  | Octagon Max-Flight 04 | 5,540 d | 5,540 g |
|  | Octagon MaxFlo | 8,670g | 8,670g |
|  | SPCA AD-480 | 15,200 e | 12,800 c |
| a The SAE Aerospace Information Report (AIR) 9968 Revision A (December 2004) viscosity method should only be used for field verification and auditing purposes; when in doubt as to which method is appropriate, use the manufacturer method. b Brookfield Spindle SC4-34/13R, small sample adapter, 10 mL of neat fluid, at 20°C, 0.3 rpm, for 15 minutes 0 seconds. c Brookfield Spindle LV2-disc with guard leg, 150 mL of neat fluid, at 20°C, 0.3 rpm, for 10 minutes 0 seconds. d Brookfield Spindle LV1 with guard leg, 500 mL of neat fluid, at 20°C, 0.3 rpm, for 33 minutes 20 seconds. e Brookfield Spindle SC4-34/13R, small sample adapter, 10 mL of neat fluid, at 20°C, 0.3 rpm, for 30 minutes 0 seconds. f Brookfield Spindle SC4-31/13R, small sample adapter, 10 mL of neat fluid, at 0°C, 0.3 rpm, for 10 minutes 0 seconds. g Brookfield Spindle LV1 with guard leg, 500 mL of neat fluid, at 20ºC, 0.3 rpm, for 10 minutes 0 seconds. |

August 2006

# SIGNIFICANCE OF TABLE 6

The viscosity values of the fluids in Table 6 are those provided by the fluid manufacturers for holdover time testing. For the holdover time guidelines to be valid, the viscosity of the undiluted fluid on the wing shall not be lower than that listed in this table. The user should periodically ensure that the viscosity of a fluid sample taken from the wing is not lower than the values listed here.

Note: Consult the fluid manufacturer for lowest on-wing viscosity associated with dilutions.

###### Table 7.  List of Qualified 1 Deicing/Anti-Icing Fluids – Winter 2006-2007

###### Qualified Type I Deicing/Anti-Icing Fluids

| Company Name | Fluid Name |
| --- | --- |
| Arkton Ltd. | Artica DG |
| Aviation Xi’an High-Tech | KHF-1 |
| Battelle | D3: Degradable by Design Deicer ADF 1006A |
| Beijing Wangye Aviation Chem. Prod. Co. | KLA-1 |
| Chemical Specialists and Development | Prist Wing Deicer |
| Clariant | Safewing MPI 1938 TF |
| Clariant | Safewing MPI 1938 TF Pre-mix |
| Clariant | Safewing MP I 1938 ECO |
| Clariant | Safewing EG I 1996 |
| Dow Chemical Company | UCAR ADF Concentrate |
| Dow Chemical Company | UCAR ADF XL-54 |
| Dow Chemical Company | UCAR PG ADF Concentrate |
| Dow Chemical Company | UCAR PG ADF Dilute 55/45 |
| HOC Industries | SafeTemp I ES |
| HOC Industries | SafeTemp I ES Plus |
| Inland Technologies | Duragly – P ready to use |
| Inland Technologies | Duragly – E ready to use |
| Kilfrost | Kilfrost DF PLUS |
| Kilfrost | Kilfrost DF PLUS (80) |
| Kilfrost | Kilfrost DF PLUS (88) |
| Lyondell Chemical Company | ARCOPlus |
| Lyondell Chemical Company | ARCTIC Plus |
| Newwave Aerochemical Company | FCY-1A |
| Octagon Process | Octaflo EF |
| Octagon Process | Octaflo EG |
| SPCA | DE-950 |
| Viterbo S.A. | Jarkleer SAE Type I |

###### Table 7.  List of Qualified (1) Deicing/Anti-Icing Fluids – Winter 2006-2007 (Continued)

###### Qualified Type II Deicing/Anti-Icing Fluids

| Company Name | Fluid Name |
| --- | --- |
| Clariant | Safewing MP II 1951 |
| Clariant | Safewing MP II 2025 ECO |
| Clariant | Safewing MP II Flight |
| Kilfrost | Kilfrost ABC-II PLUS |
| Kilfrost | Kilfrost ABC-3 |
| Kilfrost | Kilfrost ABC-2000 |
| Kilfrost | Kilfrost ABC-TF2 |
| Octagon Process | E-Max |
| SPCA | SPCA Ecowing 26 |

###### Qualified Type III Deicing/Anti-Icing Fluids

| Company Name | Fluid Name |
| --- | --- |
| Clariant | Safewing MP III 2031 ECO |

###### Qualified Type IV Deicing/Anti-Icing Fluids

| Company Name | Fluid Name |
| --- | --- |
| Clariant | Safewing MP IV 2001 |
| Clariant | Safewing MP IV 2012 Protect |
| Clariant | Safewing MP IV 2030 ECO |
| Clariant | Safewing MP IV Launch |
| Dow Chemical Company | UCAR AAF ULTRA+ |
| Dow Chemical Company | UCAR AAF AD-480 |
| Kilfrost | Kilfrost ABC-S |
| Kilfrost | Kilfrost ABC-S Plus |
| Octagon Process | Max Flight |
| Octagon Process | Max Flight 04 |
| Octagon Process | MaxFlo |

###### Table 7.  List of Qualified (1) Deicing/Anti-Icing Fluids – Winter 2006-2007 (Continued)


Qualified Type IV Deicing/Anti-Icing Fluids (Continued)

| SPCA | SPCA AD-480 |
| --- | --- |

¹ Qualified indicates that the fluid has been qualified solely to the requirements of the applicable SAE anti-icing and aerodynamic performance specifications in effect at the time of certification, as conducted by the Anti-Icing Materials International Laboratory at the University of Quebec at Chicoutimi, Canada, Web site: http://www.uqac.uquebec.ca/amil/.  For other specification requirements for Type I fluids, see SAE AMS 1424 (latest version) and for SAE Types II, III, and IV fluids, see SAE AMS 1428 (latest version). Fluids that qualify after the issuance of this list will appear in a later update.